## Slide 1: Switching and Routing Essentials CT133-3-2 SRE
VLAN

## Slide 2: Module Objectives
Module Title: Protocols and Models
Module Objective: Explain how network protocols enable devices to access local and remote network resources.
Topic Title | Topic Objective
Overview of VLANs | Explain the purpose of VLANs in a switched network.
VLANs in a Multi-Switched Environment | Explain how a switch forwards frames based on VLAN configuration in a multi-switch environment.
VLAN Configuration | Configure a switch port to be assigned to a VLAN based on requirements.
VLAN Trunks | Configure a trunk port on a LAN switch.
Dynamic Trunking Protocol | Configure Dynamic Trunking Protocol (DTP).
Notes: 2
3 – VLANs
3.0 – Introduction
3.0.2 – What will I learn to do in this module?

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to:
Explain the purpose of VLANs in a switched network.
Explain how a switched forwards frames based on the VLAN configuration in a multi-switched environment.
Identify the types of VLAN.
Configure a switch port to be assigned to a VLAN based on the requirements.
Configure the trunk port on a LAN switch.
Configure the Dynamic Trunking Protocpl (DTP)

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
VLAN
Logical broadcast domain
Data VLAN
Default VLAN
Native VLAN
Management VLAN
show vlan brief
Voice VLAN
VLAN Trunk
VLAN Segmentation
IEEE 802.1Q
VLAN Tagging
Canonical Format Identifier (CFI)
User Priority
VLAN ID
Type
show interfaces int switchport

## Slide 5: Overview of VLANs
Notes: 3 – VLANs
3.1 – Overview of VLANs

## Slide 6: Overview of VLANs VLAN Definitions
VLANs are logical connections with other similar devices.
Placing devices into various VLANs have the following characteristics:
  Provides segmentation of the various groups of devices on the same switches
  Provide organization that is more manageable
      Broadcasts, multicasts and unicasts are isolated in the individual VLAN
      Each VLAN will have its own unique range of IP addressing
      Smaller broadcast domains
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.1 – VLAN Definitions

## Slide 7: Overview of VLANs Benefits of a VLAN Design
Benefits of using VLANs are as follows:
Benefits | Description
Smaller Broadcast Domains | Dividing the LAN reduces the number of broadcast domains
Improved Security | Only users in the same VLAN can communicate together
Improved IT Efficiency | VLANs can group devices with similar requirements, e.g. faculty vs. students
Reduced Cost | One switch can support multiple groups or VLANs
Better Performance | Small broadcast domains reduce traffic, improving bandwidth
Simpler Management | Similar groups will need similar applications and other network resources
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.2 – Benefits of a VLAN Design

## Slide 8: Overview of VLANs Types of VLANs
Default VLAN
VLAN 1 is the following:
  The default VLAN
  The default Native VLAN
  The default Management VLAN
  Cannot be deleted or renamed
  Note: While we cannot delete VLAN1 Cisco will recommend that we assign these default features to other VLANs
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs

## Slide 9: Overview of VLANs Types of VLANs (Cont.)
Data VLAN
Dedicated to user-generated traffic (email and web traffic).
VLAN 1 is the default data VLAN because all interfaces are assigned to this VLAN.
Native VLAN
This is used for trunk links only.
All frames are tagged on an 802.1Q trunk link except for those on the native VLAN.
Management VLAN
This is used for SSH/Telnet VTY traffic and should not be carried with end user traffic.
Typically, the VLAN that is the SVI for the Layer 2 switch.
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs (Cont.)

## Slide 10: Overview of VLANs Types of VLANs (Cont.)
Voice VLAN
  A separate VLAN is required because Voice traffic requires:
      Assured bandwidth
      High QoS priority
      Ability to avoid congestion
      Delay less that 150 ms from source to destination
  The entire network must be designed to support voice.
Notes: 3 – VLANs
3.1 – Overview of VLANs
3.1.3 – Types of VLANs (Cont.)

## Slide 11: VLANs in a Multi-Switched Environment
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment

## Slide 12: VLANs in a Multi-Switched Environment Defining VLAN Trunks
A trunk is a point-to-point link between two network devices.
Cisco trunk functions:
Allow more than one VLAN
Extend the VLAN across the entire network
By default, supports all VLANs
Supports 802.1Q trunking
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.1 – Defining VLAN Trunks

## Slide 13: VLANs in a Multi-Switched Environment Networks without VLANs
Without VLANs, all devices connected to the switches will receive all unicast, multicast, and broadcast traffic.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.2 – Networks without VLANs

## Slide 14: VLANs in a Multi-Switched Environment Networks with VLANs
With VLANs, unicast, multicast, and broadcast traffic is confined to a VLAN. Without a Layer 3 device to connect the VLANs, devices in different VLANs cannot communicate.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.3 – Networks with VLANs

## Slide 15: VLANs in a Multi-Switched Environment VLAN Identification with a Tag
The IEEE 802.1Q header is 4 Bytes
When the tag is created the FCS must be recalculated.
When sent to end devices, this tag must be removed and the FCS recalculated back to its original number.
802.1Q VLAN Tag Field | Function
Type | 2-Byte field with hexadecimal 0x8100 This is referred to as Tag Protocol ID (TPID)
User Priority | 3-bit value that supports
Canonical Format Identifier (CFI) | 1-bit value that can support token ring frames on Ethernet
VLAN ID (VID) | 12-bit VLAN identifier that can support up to 4096 VLANs
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.4 – VLAN Identification with a Tag

## Slide 16: VLANs in a Multi-Switched Environment Native VLANs and 802.1Q Tagging
802.1Q trunk basics:
Tagging is typically done on all VLANs.
The use of a native VLAN was designed for legacy use, like the hub in the example.
Unless changed, VLAN1 is the native VLAN.
Both ends of a trunk link must be configured with the same native VLAN.
Each trunk is configured separately, so it is possible to have a different native VLANs on separate trunks.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.5 – Native VLANs and 802.1Q Tagging
Depending on the vendor, tagged ports are able to carry traffic for all VLANs by default but a filter can be applied on such ports to limit the allowed VLANs.
Hint: Cisco calls this type of ports “trunk ports“.
There is the last scenario we have not considered: what should a tagged port do if it receives an untagged packet?
Since that port can carry multiple VLANs and is not assigned to a single VLAN, what VLAN tag should it apply to that untagged packet?
This is where the Native VLAN comes in.
The Native VLAN is the VLAN associated with all untagged packets on a tagged/trunk port.

## Slide 17: VLANs in a Multi-Switched Environment Native VLANs and 802.1Q Tagging
However, if you have a hub between two switches connected with a trunk and you have a PC connected to that hub, then you will definitely receive untagged frames on the trunk ports. Take a look at the opposite diagram:
Any frames sent by the PC will hit the trunk ports on the two switches untagged. The switches must know what to do with them.
This is why the native VLAN must be configured, otherwise these frames will be dropped.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.5 – Native VLANs and 802.1Q Tagging
Depending on the vendor, tagged ports are able to carry traffic for all VLANs by default but a filter can be applied on such ports to limit the allowed VLANs.
Hint: Cisco calls this type of ports “trunk ports“.
There is the last scenario we have not considered: what should a tagged port do if it receives an untagged packet?
Since that port can carry multiple VLANs and is not assigned to a single VLAN, what VLAN tag should it apply to that untagged packet?
This is where the Native VLAN comes in.
The Native VLAN is the VLAN associated with all untagged packets on a tagged/trunk port.

## Slide 18: VLANs in a Multi-Switched Environment Voice VLAN Tagging
The VoIP phone is a three port switch:
The switch will use CDP to inform the phone of the Voice VLAN.
The phone will tag its own traffic (Voice) and can set Cost of Service (CoS). CoS is QoS for layer 2.
The phone may or may not tag frames from the PC.
Traffic | Tagging Function
Voice VLAN | tagged with an appropriate Layer 2 class of service (CoS) priority value
Access VLAN | can also be tagged with a Layer 2 CoS priority value
Access VLAN | is not tagged (no Layer 2 CoS priority value)
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.6 – Voice VLAN Tagging

## Slide 19: VLANs in a Multi-Switched Environment Voice VLAN Verification Example
The show interfaces fa0/18 switchport command can show us both data and voice VLANs assigned to the interface.
Notes: 3 – VLANs
3.2 – VLANs in a Multi-Switched Environment
3.2.7 – Voice VLAN Verification Example

## Slide 20: VLAN Configuration
Notes: 3 – VLANs
3.3 – VLAN Configuration

## Slide 21: VLAN Configuration VLAN Ranges on Catalyst Switches
  Catalyst switches 2960 and 3650 support over 4000 VLANs.
Normal Range VLAN 1 – 1005 | Extended Range VLAN 1006 - 4095
Used in Small to Medium sized businesses | Used by Service Providers
1002 – 1005 are reserved for legacy VLANs | Are in Running-Config
1, 1002 – 1005 are auto created and cannot be deleted | Supports fewer VLAN features
Stored in the vlan.dat file in flash | Requires VTP configurations
VTP can synchronize between switches | 
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.1 – VLAN Ranges on Catalyst Switches

## Slide 22: VLAN Configuration VLAN Creation Commands
  VLAN details are stored in the vlan.dat file. You create VLANs in the global configuration mode.
Task | IOS Command
Enter global configuration mode. | Switch# configure terminal
Create a VLAN with a valid ID number. | Switch(config)# vlan vlan-id
Specify a unique name to identify the VLAN. | Switch(config-vlan)# name vlan-name
Return to the privileged EXEC mode. | Switch(config-vlan)# end
Enter global configuration mode. | Switch# configure terminal
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.2 – VLAN Creation Commands

## Slide 23: VLAN Configuration VLAN Creation Example
If the Student PC is going to be in VLAN 20, we will create the VLAN first and then name it.
If you do not name it, the Cisco IOS will give it a default name of vlan and the four digit number of the VLAN. E.g. vlan0020 for VLAN 20.
Prompt | Command
S1# | Configure terminal
S1(config)# | vlan 20
S1(config-vlan)# | name student
S1(config-vlan)# | end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.3 – VLAN Creation Example

## Slide 24: VLAN Configuration VLAN Port Assignment Commands
Once the VLAN is created, we can then assign it to the correct interfaces.
Task | Command
Enter global configuration mode. | Switch# configure terminal
Enter interface configuration mode. | Switch(config)# interface interface-id
Set the port to access mode. | Switch(config-if)# switchport mode access
Assign the port to a VLAN. | Switch(config-if)# switchport access vlan vlan-id
Return to the privileged EXEC mode. | Switch(config-if)# end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.4 – VLAN Port Assignment Commands

## Slide 25: VLAN Configuration VLAN Port Assignment Example
We can assign the VLAN to the port interface.
Once the device is assigned the VLAN, then the end device will need the IP address information for that VLAN
Here, Student PC receives 172.17.20.22
Prompt | Command
S1# | Configure terminal
S1(config)# | Interface fa0/18
S1(config-if)# | Switchport mode access
S1(config-if)# | Switchport access vlan 20
S1(config-if)# | end
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.5 – VLAN Port Assignment Example

## Slide 26: VLAN Configuration Data and Voice VLANs
An access port may only be assigned to one data VLAN.
However it may also be assigned to one Voice VLAN for when a phone and an end device are off of the same switchport.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.6 – Data and Voice VLANs

## Slide 27: VLAN Configuration Data and Voice VLAN Example
We will want to create and name both Voice and Data VLANs.
In addition to assigning the data VLAN, we will also assign the Voice VLAN and turn on QoS for the voice traffic to the interface.
The newer catalyst switch will automatically create the VLAN, if it does not already exist, when it is assigned to an interface.
Note: QoS is beyond the scope of this course. Here we do show the use of the mls qos trust [cos | device cisco-phone | dscp | ip-precedence] command.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.7 – Data and Voice VLAN Example

## Slide 28: VLAN Configuration Verify VLAN Information
Use the show vlan command. The complete syntax is:
show vlan [brief | id vlan-id | name vlan-name | summary]
Task | Command Option
Display VLAN name, status, and its ports one VLAN per line. | brief
Display information about the identified VLAN ID number. | id vlan-id
Display information about the identified VLAN name. The vlan-name is an ASCII string from 1 to 32 characters. | name vlan-name
Display VLAN summary information. | summary
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.8 – Verify VLAN Information

## Slide 29: VLAN Configuration Change VLAN Port Membership
There are a number of ways to change VLAN membership:
re-enter switchport access vlan vlan-id command
use the no switchport access vlan to place interface back in VLAN 1
Use the show vlan brief or the show interface fa0/18 switchport commands to verify the correct VLAN association.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.9 – Change VLAN Port Membership

## Slide 30: VLAN Configuration Delete VLANs
Delete VLANs with the no vlan vlan-id command.
Caution: Before deleting a VLAN, reassign all member ports to a different VLAN.
Delete all VLANs with the delete flash:vlan.dat or delete vlan.dat commands.
Reload the switch when deleting all VLANs.
Note: To restore to factory default – unplug all data cables, erase the startup-configuration and delete the vlan.dat file, then reload the device.
Notes: 3 – VLANs
3.3 – VLAN Configuration
3.3.10 – Delete VLANs
3.3.11 – Syntax Checker – VLAN Configuration

## Slide 31: VLAN Trunks
Notes: 3 – VLANs
3.4 – VLAN Trunks

## Slide 32: VLAN Trunks Trunk Configuration Commands
Configure and verify VLAN trunks. Trunks are layer 2 and carry traffic for all VLANs.
Task | IOS Command
Enter global configuration mode. | Switch# configure terminal
Enter interface configuration mode. | Switch(config)# interface interface-id
Set the port to permanent trunking mode. | Switch(config-if)# switchport mode trunk
Sets the native VLAN to something other than VLAN 1. | Switch(config-if)# switchport trunk native vlan vlan-id
Specify the list of VLANs to be allowed on the trunk link. | Switch(config-if)# switchport trunk allowed vlan vlan-list
Return to the privileged EXEC mode. | Switch(config-if)# end
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.1 – Trunk Configuration Commands

## Slide 33: VLAN Trunks Trunk Configuration Example
The subnets associated with each VLAN are:
  VLAN 10 - Faculty/Staff - 172.17.10.0/24
  VLAN 20 - Students - 172.17.20.0/24
  VLAN 30 - Guests - 172.17.30.0/24
  VLAN 99 - Native - 172.17.99.0/24
F0/1 port on S1 is configured as a trunk port.
Note: This assumes a 2960 switch using 802.1q tagging. Layer 3 switches require the encapsulation to be configured before the trunk mode.
Prompt | Command
S1(config)# | Interface fa0/1
S1(config-if)# | Switchport mode trunk
S1(config-if)# | Switchport trunk native vlan 99
S1(config-if)# | Switchport trunk allowed vlan 10,20,30,99
S1(config-if)# | end
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.2 – Trunk Configuration Example

## Slide 34: VLAN Trunks Verify Trunk Configuration
Set the trunk mode and native vlan.
Notice sh int fa0/1 switchport command:
Is set to trunk administratively
Is set as trunk operationally (functioning)
Encapsulation is dot1q
Native VLAN set to VLAN 99
All VLANs created on the switch will pass traffic on this trunk
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.3 – Verify Trunk Configuration

## Slide 35: VLAN Trunks Reset the Trunk to the Default State
Reset the default trunk settings with the no command.
  All VLANs allowed to pass traffic
  Native VLAN = VLAN 1
Verify the default settings with a sh int fa0/1 switchport command.
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.4 – Reset the Trunk to the Default State

## Slide 36: VLAN Trunks Reset the Trunk to the Default State (Cont.)
Reset the trunk to an access mode with the switchport mode access command:
  Is set to an access interface administratively
  Is set as an access interface operationally (functioning)
Notes: 3 – VLANs
3.4 – VLAN Trunks
3.4.4 – Reset the Trunk to the Default State (Cont.)

## Slide 37: Dynamic Trunking Protocol
Notes: 3 – VLANs
3.5 – Dynamic Trunking Protocol

## Slide 38: Dynamic Trunking Protocol Introduction to DTP
Dynamic Trunking Protocol (DTP) is a proprietary Cisco protocol.
DTP characteristics are as follows:
  On by default on Catalyst 2960 and 2950 switches
  Dynamic-auto is default on the 2960 and 2950 switches
  May be turned off with the nonegotiate command
  May be turned back on by setting the interface to dynamic-auto
  Setting a switch to a static trunk or static access will avoid negotiation issues with the switchport mode trunk or the switchport mode access commands.
Notes: 3 – VLANs
3.5 – Dynamic Trunking Protocol
3.5.1 – Introduction to DTP

## Slide 39: Dynamic Trunking Protocol Negotiated Interface Modes
The switchport mode command has additional options.
Use the switchport nonegotiate interface configuration command to stop DTP negotiation.
Option | Description
access | Permanent access mode and negotiates to convert the neighboring link into an access link
dynamic auto | Will becomes a trunk interface if the neighboring interface is set to trunk or desirable mode
dynamic desirable | Actively seeks to become a trunk by negotiating with other auto or desirable interfaces
trunk | Permanent trunking mode and negotiates to convert the neighboring link into a trunk link
Notes: 3 – VLANs
3.5 – Dynamic Trunking Protocol
3.5.2 – Negotiated Interface Modes

## Slide 40: Dynamic Trunking Protocol Results of a DTP Configuration
DTP configuration options are as follows:
 | Dynamic Auto | Dynamic Desirable | Trunk | Access
Dynamic Auto | Access | Trunk | Trunk | Access
Dynamic Desirable | Trunk | Trunk | Trunk | Access
Trunk | Trunk | Trunk | Trunk | Limited connectivity
Access | Access | Access | Limited connectivity | Access
Notes: 3 – VLANs
3.5 – Dynamic Trunking Protocol
3.5.3 – Results of a DTP Configuration

## Slide 41: Dynamic Trunking Protocol Verify DTP Mode
The default DTP configuration is dependent on the Cisco IOS version and platform.
Use the show dtp interface command to determine the current DTP mode.
Best practice recommends that the interfaces be set to access or trunk and to turnoff DTP
Notes: 3 – VLANs
3.5 – Dynamic Trunking Protocol
3.5.4 – Verify DTP Mode

## Slide 42: Module Practice and Quiz
Notes: 3 – VLANs
3.6 – Module Practice and Quiz

## Slide 43: Quick Review Question
Refer to Quiz - Chapter 3 in Cisco Networking Academy platform
In the Packet Tracer activity, you will perform the following:
Configure VLANs
Assign Ports to VLANs
Configure Static Trunking
Configure Dynamic Trunking
In the lab, you will perform the following:
  Build the Network and Configure Basic Device Settings
  Create VLANs and Assign Switch Ports
  Configure an 802.1Q Trunk between the Switches

## Slide 44
    VLANs are based on logical instead of physical connections.
    VLANs can segment networks based on function, team, or application.
    Each VLAN is considered a separate logical network.
    A trunk is a point-to-point link that carries more than one VLAN.
    VLAN tag fields include the type, user priority, CFI and VID.
    A separate voice VLAN is required to support VoIP.
    Normal range VLAN configurations are stored in the vlan.dat file in flash.
    An access port can belong to one data VLAN at a time, but may also have a Voice VLAN.
Summary of Main Teaching Points
Notes: All switch ports (interfaces) should be secured before the switch is deployed for production use.
By default, Layer 2 switch ports are set to dynamic auto (trunking on).
The simplest and most effective method to prevent MAC address table overflow attacks is to enable port security.
The switch can be configured to learn about MAC addresses on a secure port in one of three ways: manually configured, dynamically learned, and dynamically learned – sticky.
If the MAC address of a device attached to the port differs from the list of secure addresses, then a port violation occurs. By default, the port enters the error-disabled state. When a port is placed in the error-disabled state, no traffic is sent or received on that port.
Mitigate VLAN Hopping attacks by disabling DTP negotiations, disabling unused ports, manually setting trunking where required, and using a native VLAN other than VLAN 1.

## Slide 45
    A trunk is a Layer 2 link between two switches that carries traffic for all VLANs.
    Trunks will need tagging for the various VLANs, typically 802.1q .
    IEEE 802.1q tagging makes provision for one native VLAN that will remain untagged.
    An interface can be set to trunking or nontrunking.
    Trunk negotiation is managed by the Dynamic Trunking Protocol (DTP).
    DTP is a Cisco proprietary protocol that manages trunk negotiations.
Summary of Main Teaching Points
Notes: The goal of a DHCP starvation attack is to create a Denial of Service (DoS) for connecting clients. DHCP spoofing attacks can be mitigated by using DHCP snooping on trusted ports.
DHCP snooping determines whether DHCP messages are from an administratively-configured trusted or untrusted source. It then filters DHCP messages and rate-limits DHCP traffic from untrusted sources.
Dynamic ARP inspection (DAI) requires DHCP snooping and helps prevent ARP attacks by verifying ARP traffic.
Implement Dynamic ARP Inspection to mitigate ARP spoofing and ARP poisoning.
To mitigate Spanning Tree Protocol (STP) manipulation attacks, use PortFast and Bridge Protocol Data Unit (BPDU) Guard.

## Slide 46: Question and Answer Session
Q & A

## Slide 47: What we will cover next
VLANs Trunking