## Slide 1: Switching and Routing Essentials CT133-3-2 SRE
INTER-VLAN ROUTING

## Slide 2: Module Objectives
Module Title: Inter-VLAN Routing
Module Objective: Troubleshoot inter-VLAN routing on Layer 3 devices
Topic Title | Topic Objective
Inter-VLAN Routing Operation | Describe options for configuring inter-VLAN routing.
Router-on-a-Stick Inter-VLAN Routing | Configure router-on-a-stick inter-VLAN routing.
Inter-VLAN Routing using Layer 3 Switches | Configure inter-VLAN routing using Layer 3 switching.
Notes: 2

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to:
Describe options for configuring inter-VLAN routing.
Configure router-on-a-stick inter-VLAN routing.
Configure inter-VLAN routing using Layer 3 switching.

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
Inter-VLAN Routing
Router-on-a-Stick
encapsulation dot1q X [ native ]
no switchport
router ospf
ip routing

## Slide 5: Inter-VLAN Routing Operation
Notes: 4- Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation

## Slide 6: Inter-VLAN Routing Operation What is Inter-VLAN Routing?
VLANs are used to segment switched Layer 2 networks for a variety of reasons. Regardless of the reason, hosts in one VLAN cannot communicate with hosts in another VLAN unless there is a router or a Layer 3 switch to provide routing services.
Inter-VLAN routing is the process of forwarding network traffic from one VLAN to another VLAN.
There are three inter-VLAN routing options:
  Legacy Inter-VLAN routing - This is a legacy solution. It does not scale well.
  Router-on-a-Stick - This is an acceptable solution for a small to medium-sized network.
  Layer 3 switch using switched virtual interfaces (SVIs) - This is the most scalable solution for medium to large organizations.
Notes: 4 – Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation
4.1.1 - What is Inter-VLAN Routing?

## Slide 7: Inter-VLAN Routing Operation Legacy Inter-VLAN Routing
The first inter-VLAN routing solution relied on using a router with multiple Ethernet interfaces. Each router interface was connected to a switch port in different VLANs. The router interfaces served as the default gateways to the local hosts on the VLAN subnet.
Legacy inter-VLAN routing using physical interfaces works, but it has a significant limitation. It is not reasonably scalable because routers have a limited number of physical interfaces. Requiring one physical router interface per VLAN quickly exhausts the physical interface capacity of a router.
Note: This method of inter-VLAN routing is no longer implemented in switched networks and is included for explanation purposes only.
Notes: 4 – Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation
4.1.2 – Legacy Inter-VLAN Routing

## Slide 8: Inter-VLAN Routing Operation Router-on-a-Stick Inter-VLAN Routing
The ‘router-on-a-stick’ inter-VLAN routing method overcomes the limitation of the legacy inter-VLAN routing method. It only requires one physical Ethernet interface to route traffic between multiple VLANs on a network.
A Cisco IOS router Ethernet interface is configured as an 802.1Q trunk and connected to a trunk port on a Layer 2 switch. Specifically, the router interface is configured using subinterfaces to identify routable VLANs.
The configured subinterfaces are software-based virtual interfaces. Each is associated with a single physical Ethernet interface. Subinterfaces are configured in software on a router. Each subinterface is independently configured with an IP address and VLAN assignment. Subinterfaces are configured for different subnets that correspond to their VLAN assignment. This facilitates logical routing.
When VLAN-tagged traffic enters the router interface, it is forwarded to the VLAN subinterface. After a routing decision is made based on the destination IP network address, the router determines the exit interface for the traffic. If the exit interface is configured as an 802.1q subinterface, the data frames are VLAN-tagged with the new VLAN and sent back out the physical interface
Note: The router-on-a-stick method of inter-VLAN routing does not scale beyond 50 VLANs.
Notes: 4 – Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation
4.1.3 – Router-on-a-Stick Inter-VLAN Routing

## Slide 9: Inter-VLAN Routing Operation Inter-VLAN Routing on a Layer 3 Switch
The modern method of performing inter-VLAN routing is to use Layer 3 switches and switched virtual interfaces (SVI). An SVI is a virtual interface that is configured on a Layer 3 switch, as shown in the figure.
Note: A Layer 3 switch is also called a multilayer switch as it operates at Layer 2 and Layer 3. However, in this course we use the term Layer 3 switch.
Notes: 4 – Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation
4.1.4 - Inter-VLAN Routing on a Layer 3 Switch

## Slide 10: Inter-VLAN Routing Operation Inter-VLAN Routing on a Layer 3 Switch (Cont.)
Inter-VLAN SVIs are created the same way that the management VLAN interface is configured. The SVI is created for a VLAN that exists on the switch. Although virtual, the SVI performs the same functions for the VLAN as a router interface would. Specifically, it provides Layer 3 processing for packets that are sent to or from all switch ports associated with that VLAN.
The following are advantages of using Layer 3 switches for inter-VLAN routing:
  They are much faster than router-on-a-stick because everything is hardware switched and routed.
  There is no need for external links from the switch to the router for routing.
  They are not limited to one link because Layer 2 EtherChannels can be used as trunk links between the switches to increase bandwidth.
  Latency is much lower because data does not need to leave the switch in order to be routed to a different network.
  They more commonly deployed in a campus LAN than routers.
  The only disadvantage is that Layer 3 switches are more expensive.
Notes: 4 – Inter-VLAN Routing
4.1 – Inter-VLAN Routing Operation
4.1.4 - Inter-VLAN Routing on a Layer 3 Switch (Cont.)
4.1.5 – Check Your Understanding – Inter-VLAN Routing Operation

## Slide 11: Router-on-a-Stick Inter-VLAN Routing
Notes: 4- Inter-VLAN Routing
4.2 – Router-on-a-Stick Inter-VLAN Routing

## Slide 12: Router-on-a-Stick Inter-VLAN Routing Router-on-a-Stick Scenario
In the figure, the R1 GigabitEthernet 0/0/1 interface is connected to the S1 FastEthernet 0/5 port. The S1 FastEthernet 0/1 port is connected to the S2 FastEthernet 0/1 port. These are trunk links that are required to forward traffic within and between VLANs.
To route between VLANs, the R1 GigabitEthernet 0/0/1 interface is logically divided into three subinterfaces, as shown in the table. The table also shows the three VLANs that will be configured on the switches.
Assume that R1, S1, and S2 have initial basic configurations. Currently, PC1 and PC2 cannot ping each other because they are on separate networks. Only S1 and S2 can ping each other, but they but are unreachable by PC1 or PC2 because they are also on different networks.
To enable devices to ping each other, the switches must be configured with VLANs and trunking, and the router must be configured for inter-VLAN routing.
Subinterface | VLAN | IP Address
G0/0/1.10 | 10 | 192.168.10.1/24
G0/0/1.20 | 20 | 192.168.20.1/24
G0/0/1.30 | 99 | 192.168.99.1/24
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.1 – Router-on-a-Stick Scenario

## Slide 13: Router-on-a-Stick Inter-VLAN Routing S1 VLAN and Trunking Configuration
Complete the following steps to configure S1 with VLANs and trunking:
Step 1. Create and name the VLANs.
Step 2. Create the management interface.
Step 3. Configure access ports.
Step 4. Configure trunking ports.
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.2 – S1 VLAN and Trunking Configuration

## Slide 14: Router-on-a-Stick Inter-VLAN Routing S2 VLAN and Trunking Configuration
The configuration for S2 is similar to S1.
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.3 – S2 VLAN and Trunking Configuration

## Slide 15: Router-on-a-Stick Inter-VLAN Routing R1 Subinterface Configuration
The router-on-a-stick method requires you to create a subinterface for each VLAN to be routed. A subinterface is created using the interface interface_id subinterface_id global configuration mode command.
Each subinterface is then configured with the following two commands:
  encapsulation dot1q vlan_id [native] - This command configures the subinterface to respond to 802.1Q encapsulated traffic from the specified vlan-id. The native keyword option is only appended to set the native VLAN to something other than VLAN 1.
  ip address ip-address subnet-mask - This command configures the IPv4 address of the subinterface. This address typically serves as the default gateway for the identified VLAN.
Repeat the process for each VLAN to be routed. When all subinterfaces have been created, enable the physical interface using the no shutdown interface configuration command. If the physical interface is disabled, all subinterfaces are disabled.
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.4 – R1 Subinterface Configuration

## Slide 16: Router-on-a-Stick Inter-VLAN Routing R1 Subinterface Configuration (Cont.)
In the configuration, the R1 G0/0/1 subinterfaces are configured for VLANs 10, 20, and 99.
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.4 – R1 Subinterface Configuration (Cont.)

## Slide 17: Router-on-a-Stick Inter-VLAN Routing Verify Connectivity Between PC1 and PC2
The router-on-a-stick configuration is complete after the switch trunk and the router subinterfaces have been configured. The configuration can be verified from the hosts, router, and switch.
From a host, verify connectivity to a host in another VLAN using the ping command. It is a good idea to first verify the current host IP configuration using the ipconfig Windows host command.
Next, use ping to verify connectivity with PC2 and S1, as shown in the figure. The ping output successfully confirms inter-VLAN routing is operating.
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.5 – Verify Connectivity Between PC1 and PC2

## Slide 18: Router-on-a-Stick Inter-VLAN Routing Router-on-a-Stick Inter-VLAN Routing Verification
In addition to using ping between devices, the following show commands can be used to verify and troubleshoot the router-on-a-stick configuration.
show ip route
show ip interface brief
show interfaces
show interfaces trunk
Notes: 4 – Inter-VLAN Routing
4.2 - Router-on-a-Stick Inter-VLAN Routing
4.2.6 – Router-on-a-Stick Inter-VLAN Routing Verification

## Slide 19: Inter-VLAN Routing using Layer 3 Switches
Notes: 4- Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches

## Slide 20: Inter-VLAN Routing using Layer 3 Switches Layer 3 Switch Inter-VLAN Routing
Inter-VLAN routing using the router-on-a-stick method is simple to implement for a small to medium-sized organization. However, a large enterprise requires a faster, much more scalable method to provide inter-VLAN routing.
Enterprise campus LANs use Layer 3 switches to provide inter-VLAN routing. Layer 3 switches use hardware-based switching to achieve higher-packet processing rates than routers. Layer 3 switches are also commonly implemented in enterprise distribution layer wiring closets.
Capabilities of a Layer 3 switch include the ability to do the following:
  Route from one VLAN to another using multiple switched virtual interfaces (SVIs).
  Convert a Layer 2 switchport to a Layer 3 interface (i.e., a routed port). A routed port is similar to a physical interface on a Cisco IOS router.
  To provide inter-VLAN routing, Layer 3 switches use SVIs. SVIs are configured using the same interface vlan vlan-id command used to create the management SVI on a Layer 2 switch. A Layer 3 SVI must be created for each of the routable VLANs.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.1 – Layer 3 Switch Inter-VLAN Routing

## Slide 21: Inter-VLAN Routing using Layer 3 Switches Layer 3 Switch Scenario
In the figure, the Layer 3 switch, D1, is connected to two hosts on different VLANs. PC1 is in VLAN 10 and PC2 is in VLAN 20, as shown. The Layer 3 switch will provide inter-VLAN routing services to the two hosts.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.2 – Layer 3 Switch Scenario

## Slide 22: Inter-VLAN Routing using Layer 3 Switches Layer 3 Switch Configuration
Complete the following steps to configure S1 with VLANs and trunking:
Step 1. Create the VLANs. In the example, VLANs 10 and 20 are used.
Step 2. Create the SVI VLAN interfaces. The IP address configured will serve as the default gateway for hosts in the respective VLAN.
Step 3. Configure access ports. Assign the appropriate port to the required VLAN.
Step 4. Enable IP routing. Issue the ip routing global configuration command to allow traffic to be exchanged between VLANs 10 and 20. This command must be configured to enable inter-VAN routing on a Layer 3 switch for IPv4.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.3 – Layer 3 Switch Configuration

## Slide 23: Inter-VLAN Routing using Layer 3 Switches Layer 3 Switch Inter-VLAN Routing Verification
Inter-VLAN routing using a Layer 3 switch is simpler to configure than the router-on-a-stick method. After the configuration is complete, the configuration can be verified by testing connectivity between the hosts.
From a host, verify connectivity to a host in another VLAN using the ping command. It is a good idea to first verify the current host IP configuration using the ipconfig Windows host command.
Next, verify connectivity with PC2 using the ping Windows host command. The successful ping output confirms inter-VLAN routing is operating.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.4 – Layer 3 Switch Inter-VLAN Routing Verification

## Slide 24: Inter-VLAN Routing using Layer 3 Switches Routing on a Layer 3 Switch
If VLANs are to be reachable by other Layer 3 devices, then they must be advertised using static or dynamic routing. To enable routing on a Layer 3 switch, a routed port must be configured.
A routed port is created on a Layer 3 switch by disabling the switchport feature on a Layer 2 port that is connected to another Layer 3 device. Specifically, configuring the no switchport interface configuration command on a Layer 2 port converts it into a Layer 3 interface. Then the interface can be configured with an IPv4 configuration to connect to a router or another Layer 3 switch.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.5 - Routing on a Layer 3 Switch

## Slide 25: Inter-VLAN Routing using Layer 3 Switches Routing Scenario on a Layer 3 Switch
In the figure, the previously configured D1 Layer 3 switch is now connected to R1. R1 and D1 are both in an Open Shortest Path First (OSPF) routing protocol domain. Assume inter-VLAN has been successfully implemented on D1. The G0/0/1 interface of R1 has also been configured and enabled. Additionally, R1 is using OSPF to advertise its two networks, 10.10.10.0/24 and 10.20.20.0/24.
Note: OSPF routing configuration is covered in another course. In this module, OSPF configuration commands will be given to you in all activities and assessments. It is not required that you understand the configuration in order to enable OSPF routing on the Layer 3 switch.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.6 - Routing Scenario on a Layer 3 Switch

## Slide 26: Inter-VLAN Routing using Layer 3 Switches Routing Configuration on a Layer 3 Switch
Complete the following steps to configure D1 to route with R1:
Step 1. Configure the routed port. Use the no switchport command to convert the port to a routed port, then assign an IP address and subnet mask. Enable the port.
Step 2. Enable routing. Use the ip routing global configuration command to enable routing.
Step 3. Configure routing. Use an appropriate routing method. In this example, Single-Area OSPFv2 is configured
Step 4. Verify routing. Use the show ip route command.
Step 5. Verify connectivity. Use the ping command to verify reachability.
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.7 – Routing Configuration on a Layer 3 Switch

## Slide 27: Inter-VLAN Routing using Layer 3 Switches Packet Tracer – Configure Layer 3 Switching and inter-VLAN Routing
In this Packet Tracer, you will complete the following objectives:
Part 1: Configure Layer 3 Switching
Part 2: Configure Inter-VLAN Routing
Part 3: Configure IPv6 Inter-VLAN Routing
Notes: 4 – Inter-VLAN Routing
4.3 – Inter-VLAN Routing using Layer 3 Switches
4.3.7 – Packet Tracer – Configure Layer 3 Switch and Inter-VLAN Routing

## Slide 28: Module Practice and Quiz
Notes: 4- Inter-VLAN Routing
4.5 – Module Practice and Quiz

## Slide 29: Quick Review Question
Refer to Quiz - Chapter 4 in Cisco Networking Academy platform
In this lab, you will complete the following objectives:
Part 1: Build the Network and Configure Basic Device Settings
Part 2: Create VLANs and Assign Switch Ports
Part 3: Configure an 802.1Q Trunk between the Switches
Part 4: Configure Inter-VLAN Routing on the S1 Switch
Part 5: Verify Inter-VLAN Routing is Working

## Slide 30
    Inter-VLAN routing is the process of forwarding network traffic from one VLAN to another VLAN.
    Three options include legacy, router-on-a-stick, and Layer 3 switch using SVIs.
    To configure a switch with VLANs and trunking, complete the following steps: create and name the VLANs, create the management interface, configure access ports, and configure trunking ports.
    The router-on-a-stick method requires a subinterface to be created for each VLAN to be routed. A subinterface is created using the interface interface_id subinterface_id global configuration mode command.
    Each router subinterface must be assigned an IP address on a unique subnet for routing to occur. When all subinterfaces have been created, the physical interface must be enabled using the no shutdown interface configuration command.
Summary of Main Teaching Points
Notes: All switch ports (interfaces) should be secured before the switch is deployed for production use.
By default, Layer 2 switch ports are set to dynamic auto (trunking on).
The simplest and most effective method to prevent MAC address table overflow attacks is to enable port security.
The switch can be configured to learn about MAC addresses on a secure port in one of three ways: manually configured, dynamically learned, and dynamically learned – sticky.
If the MAC address of a device attached to the port differs from the list of secure addresses, then a port violation occurs. By default, the port enters the error-disabled state. When a port is placed in the error-disabled state, no traffic is sent or received on that port.
Mitigate VLAN Hopping attacks by disabling DTP negotiations, disabling unused ports, manually setting trunking where required, and using a native VLAN other than VLAN 1.

## Slide 31
    Enterprise campus LANs use Layer 3 switches to provide inter-VLAN routing. Layer 3 switches use hardware-based switching to achieve higher-packet processing rates than routers.
    Capabilities of a Layer 3 switch include routing from one VLAN to another using multiple switched virtual interfaces (SVIs) and converting a Layer 2 switchport to a Layer 3 interface (i.e., a routed port).
    To provide inter-VLAN routing, Layer 3 switches use SVIs. SVIs are configured using the same interface vlan vlan-id command used to create the management SVI on a Layer 2 switch.
Summary of Main Teaching Points
Notes: The goal of a DHCP starvation attack is to create a Denial of Service (DoS) for connecting clients. DHCP spoofing attacks can be mitigated by using DHCP snooping on trusted ports.
DHCP snooping determines whether DHCP messages are from an administratively-configured trusted or untrusted source. It then filters DHCP messages and rate-limits DHCP traffic from untrusted sources.
Dynamic ARP inspection (DAI) requires DHCP snooping and helps prevent ARP attacks by verifying ARP traffic.
Implement Dynamic ARP Inspection to mitigate ARP spoofing and ARP poisoning.
To mitigate Spanning Tree Protocol (STP) manipulation attacks, use PortFast and Bridge Protocol Data Unit (BPDU) Guard.

## Slide 32: Question and Answer Session
Q & A

## Slide 33: What we will cover next
STP Concepts