## Slide 1: Switching and Routing Essentials CT122-3-2 SRE
Routing Concepts

## Slide 2: Topic & Structure of The Lesson
Topic Title | Topic Objective
Path Determination | Explain how routers determine the best path.
Packet Forwarding | Explain how routers forward packets to the destination.
Basic Router Configuration Review | Configure basic settings on a router.
IP Routing Table | Describe the structure of a routing table.
Static and Dynamic Routing | Compare static and dynamic routing concepts.
Module Title: Routing Concepts
Module Objective: Explain how routers use information in packets to make forwarding decisions.

## Slide 3: Learning Outcomes
At the end of this topic, You should be able to:
    Explain how routers determine the best path.
    Explain how routers forward packets to the destination.
    Configure basic settings on a router.
    Describe the structure of a routing table.
    Compare static and dynamic routing concepts.
Notes: The following guidelines and restrictions are useful for configuring EtherChannel:
  All Ethernet interfaces on all modules must support EtherChannel with no requirement that interfaces be physically contiguous, or on the same module.
  Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode.
  All interfaces in the EtherChannel bundle must be assigned to the same VLAN or be configured as a trunk.
  An EtherChannel supports the same allowed range of VLANs on all the interfaces in a trunking EtherChannel.
Configuring EtherChannel with LACP requires three steps:
  Step 1. Specify the interfaces that compose the EtherChannel group using the interface range interface global configuration mode command.
  Step 2. Create the port channel interface with the channel-group identifier mode active command in interface range configuration mode.
  Step 3. To change Layer 2 settings on the port channel interface, enter port channel interface configuration mode using the interface port-channel command, followed by the interface identifier.
  ==================
To increase bandwidth or redundancy, multiple links could be connected between devices. However, STP will block redundant links to prevent switching loops. EtherChannel is a link aggregation technology that allows redundant links between devices that will not be blocked by STP.
EtherChannel groups multiple physical Ethernet links together into one single logical link. It provides fault-tolerance, load sharing, increased bandwidth, and redundancy between switches, routers, and servers.
When an EtherChannel is configured, the resulting virtual interface is called a port channel.
EtherChannels can be formed through negotiation using one of two protocols, PAgP or LACP. These protocols allow ports with similar characteristics to form a channel through dynamic negotiation with adjoining switches.
When an EtherChannel link is configured using Cisco-proprietary PAgP, PAgP packets are sent between EtherChannel-capable ports to negotiate the forming of a channel. Modes for PAgP are On, PAgP desirable, and PAgP auto.
LACP performs a function similar to PAgP with Cisco EtherChannel. Because LACP is an IEEE standard, it can be used to facilitate EtherChannels in multivendor environments. Modes for LACP are On, LACP active, and LACP passive.
==============
There are a number of commands to verify an EtherChannel configuration including show interfaces port-channel, show etherchannel summary, show etherchannel port-channel, and show interfaces etherchannel.
Common EtherChannel issues include the following:
  Assigned ports in the EtherChannel are not part of the same VLAN, or not configured as trunks.
  Ports with different native VLANs cannot form an EtherChannel.
  Trunking was configured on some of the ports that make up the EtherChannel, but not all of them.
  If the allowed range of VLANs is not the same, the ports do not form an EtherChannel even when PAgP is set to the auto or desirable mode.
  The dynamic negotiation options for PAgP and LACP are not compatibly configured on both ends of the EtherChannel.

## Slide 4: Key Terms You Must Be Able To Use
If you have mastered this topic, you should be able to use the following terms correctly in your assignments and exams:
best path
longest match
prefix length
next-hop router
process switching
fast switching
Cisco Express Forwarding (CEF)
route sources
static routes
dynamic routing protocols
ip route, Default Route
ip route 0.0.0.0 0.0.0.0 [ exit-if | next-hop-ip ]
ipv6 route ::/0 [ exit-if | next-hop-ipv6 ]
Administrative Distance
RIPv2, OSPFv2
EIGRP, EIGRP for IPv6
OSPFv3, IS-IS
Notes: channel-group X mode [ desirable | auto | active | passive ]
interface port-channel X
show interfaces port-channel
show etherchannel summary
show etherchannel port-channel
show interfaces etherchannel

## Slide 5: Path Determination
Notes: 14 - Routing Concepts
14.1 - Path Determination

## Slide 6: Path Determination Two Functions of a Router
When a router receives an IP packet on one interface, it determines which interface to use to forward the packet to the destination. This is known as routing.
The interface that the router uses to forward the packet may be the final destination, or it may be a network connected to another router that is used to reach the destination network.
The primary functions of a router are to determine the best path to forward packets based on the information in its routing table, and to forward packets toward their destination.
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.1 - Two Functions of a Router

## Slide 7: Path Determination Router Functions Example
The router uses its IP routing table to determine which path (route) to use to forward a packet. R1 and R2 will use their respective IP routing tables to first determine the best path, and then forward the packet.
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.2 - Router Functions Example

## Slide 8: Path Determination Best Path Equals Longest Match
The best path in the routing table is also known as the longest match.
The routing table contains route entries consisting of a prefix (network address) and prefix length. For there to be a match between the destination IP address of a packet and a route in the routing table, a minimum number of far-left bits must match between the IP address of the packet and the route in the routing table. The prefix length of the route in the routing table is used to determine the minimum number of far-left bits that must match.
The longest match is the route in the routing table that has the greatest number of far-left matching bits with the destination IP address of the packet. The longest match is always the preferred route.
Note: The term prefix length will be used to refer to the network portion of both IPv4 and IPv6 addresses.
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.3 - Best Path Equals Longest Match

## Slide 9: Path Determination IPv4 Longest Match Example
In the table, an IPv4 packet has the destination IPv4 address 172.16.0.10. The router has three route entries in its IPv4 routing table that match this packet: 172.16.0.0/12, 172.16.0.0/18, and 172.16.0.0/26. Of the three routes, 172.16.0.0/26 has the longest match and would be chosen to forward the packet. For any of these routes to be considered a match there must be at least the number of matching bits indicated by the subnet mask of the route.
Destination IPv4 Address |  | Address in Binary
172.16.0.10 |  | 10101100.00010000.00000000.00001010
Route Entry | Prefix/Prefix Length | Address in Binary
1 | 172.16.0.0/12 | 10101100.00010000.00000000.00001010
2 | 172.16.0.0/18 | 10101100.00010000.00000000.00001010
3 | 172.16.0.0/26 | 10101100.00010000.00000000.00001010
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.4 - IPv4 Longest Match Example

## Slide 10: Path Determination IPv6 Longest Match Example
An IPv6 packet has the destination IPv6 address 2001:db8:c000::99. This example shows three route entries, but only two of them are a valid match, with one of those being the longest match. The first two route entries have prefix lengths that have the required number of matching bits as indicated by the prefix length. The third route entry is not a match because its /64 prefix requires 64 matching bits.
Destination | 2001:db8:c000::99/48 | 
Route Entry | Prefix/Prefix Length | Does it match?
1 | 2001:db8:c000::/40 | Match of 40 bits
2 | 2001:db8:c000::/48 | Match of 48 bits (longest match)
3 | 2001:db8:c000:5555::/64 | Does not match 64 bits
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.5 - IPv6 Longest Match Example

## Slide 11: Path Determination Build the Routing Table
Directly Connected Networks: Added to the routing table when a local interface is configured with an IP address and subnet mask (prefix length) and is active (up and up).
Remote Networks: Networks that are not directly connected to the router. Routers learn about remote networks in two ways:
  Static routes - Added to the routing table when a route is manually configured.
  Dynamic routing protocols - Added to the routing table when routing protocols dynamically learn about the remote network.
Default Route: Specifies a next-hop router to use when the routing table does not contain a specific route that matches the destination IP address. The default route can be entered manually as a static route, or learned automatically from a dynamic routing protocol.
  A default route has a /0 prefix length. This means that no bits need to match the destination IP address for this route entry to be used. If there are no routes with a match longer than 0 bits, the default route is used to forward the packet. The default route is sometimes referred to as a gateway of last resort.
Notes: 14 - Routing Concepts
14.1 - Path Determination
14.1.6 - Build the Routing Table
14.1.7 - Check Your Understanding - Path Determination

## Slide 12: Packet Forwarding
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding

## Slide 13: Packet Forwarding Packet Forwarding Decision Process
The data link frame with an encapsulated IP packet arrives on the ingress interface.
The router examines the destination IP address in the packet header and consults its IP routing table.
The router finds the longest matching prefix in the routing table.
The router encapsulates the packet in a data link frame and forwards it out the egress interface. The destination could be a device connected to the network or a next-hop router.
However, if there is no matching route entry the packet is dropped.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.1 - Packet Forwarding Decision Process

## Slide 14: Packet Forwarding Packet Forwarding Decision Process (Cont.)
After a router has determined the best path, it could do the following:
Forward the Packet to a Device on a Directly Connected Network
If the route entry indicates that the egress interface is a directly connected network, the packet can be forwarded directly to the destination device. Typically this is an Ethernet LAN.
To encapsulate the packet in the Ethernet frame, the router needs to determine the destination MAC address associated with the destination IP address of the packet. The process varies based on whether the packet is an IPv4 or IPv6 packet.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.1 - Packet Forwarding Decision Process (Cont.)

## Slide 15: Packet Forwarding Packet Forwarding Decision Process (Cont.)
After a router has determined the best path, it could do the following:
Forward the Packet to a Next-Hop Router
If the route entry indicates that the destination IP address is on a remote network, meaning a device on network that is not directly connected. The packet must be forwarded to the next-hop router. The next-hop address is indicated in the route entry.
If the forwarding router and the next-hop router are on an Ethernet network, a similar process (ARP and ICMPv6 Neighbor Discovery) will occur for determining the destination MAC address of the packet as described previously. The difference is that the router will search for the IP address of the next-hop router in its ARP table or neighbor cache, instead of the destination IP address of the packet.
Note: This process will vary for other types of Layer 2 networks.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.1 - Packet Forwarding Decision Process (Cont.)

## Slide 16: Packet Forwarding Packet Forwarding Decision Process (Cont.)
After a router has determined the best path, it could do the following:
Drop the Packet - No Match in Routing Table
If there is no match between the destination IP address and a prefix in the routing table, and if there is no default route, the packet will be dropped.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.1 - Packet Forwarding Decision Process (Cont.)

## Slide 17: Packet Forwarding End-to-End Packet Forwarding
The primary responsibility of the packet forwarding function is to encapsulate packets in the appropriate data link frame type for the outgoing interface. For example, the data link frame format for a serial link could be Point-to-Point (PPP) protocol, High-Level Data Link Control (HDLC) protocol, or some other Layer 2 protocol.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.2 - End-to-End Packet Forwarding

## Slide 18: Packet Forwarding Packet Forwarding Mechanisms
The primary responsibility of the packet forwarding function is to encapsulate packets in the appropriate data link frame type for the outgoing interface. The more efficiently a router can perform this task, the faster packets can be forwarded by the router.
Routers support the following three packet forwarding mechanisms:
Process switching
Fast switching
Cisco Express Forwarding (CEF)
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.3 - Packet Forwarding Mechanisms

## Slide 19: Packet Forwarding Packet Forwarding Mechanisms (Cont.)
Process Switching: An older packet forwarding mechanism still available for Cisco routers. When a packet arrives on an interface, it is forwarded to the control plane where the CPU matches the destination address with an entry in its routing table, and then determines the exit interface and forwards the packet. It is important to understand that the router does this for every packet, even if the destination is the same for a stream of packets.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.3 - Packet Forwarding Mechanisms (Cont.)

## Slide 20: Packet Forwarding Packet Forwarding Mechanisms (Cont.)
Fast Switching: Was the successor to process switching. Fast switching uses a fast-switching cache to store next-hop information. When a packet arrives on an interface, it is forwarded to the control plane where the CPU searches for a match in the fast-switching cache. If it is not there, it is process-switched and forwarded to the exit interface. The flow information for the packet is then stored in the fast-switching cache. If another packet going to the same destination arrives on an interface, the next-hop information in the cache is re-used without CPU intervention.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.3 - Packet Forwarding Mechanisms (Cont.)

## Slide 21: Packet Forwarding Packet Forwarding Mechanisms (Cont.)
Cisco Express Forwarding (CEF): The most recent and default Cisco IOS packet-forwarding mechanism. CEF builds a Forwarding Information Base (FIB), and an adjacency table. The table entries are not packet-triggered like fast switching but change-triggered, such as when something changes in the network topology. When a network has converged, the FIB and adjacency tables contain all the information that a router would have to consider when forwarding a packet.
Notes: 14 - Routing Concepts
14.2 - Packet Forwarding
14.2.3 - Packet Forwarding Mechanisms (Cont.)
14.2.4 - Check Your Understanding - Packet Forwarding

## Slide 22: IP Routing Table
Notes: 14 - Routing Concepts
14.4 - IP Routing Table

## Slide 23: IP Routing Table Route Sources
A routing table contains a list of routes to known networks (prefixes and prefix lengths). The source of this information is derived from the following:
Directly connected networks
Static routes
Dynamic routing protocols
The source for each route in the routing table is identified by a code. Common codes include the following:
  L - Identifies the address assigned to a router interface.
  C - Identifies a directly connected network.
  S - Identifies a static route created to reach a specific network.
  O - Identifies a dynamically learned network from another router using the OSPF routing protocol.
  * - This route is a candidate for a default route.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.1 - Route Sources

## Slide 24: IP Routing Table Routing Table Principles
There are three routing table principles as described in the table. These are issues that are addressed by the proper configuration of dynamic routing protocols or static routes on all the routers between the source and destination devices.
Routing Table Principle | Example
Every router makes its decision alone, based on the information it has in its own routing table. | R1 can only forward packets using its own routing table. R1 does not know what routes are in the routing tables of other routers (e.g., R2).
The information in a routing table of one router does not necessarily match the routing table of another router. | Just because R1 has route in its routing table to a network in the internet via R2, that does not mean that R2 knows about that same network.
Routing information about a path does not provide return routing information. | R1 receives a packet with the destination IP address of PC1 and the source IP address of PC3. Just because R1 knows to forward the packet out its G0/0/0 interface, doesn’t necessarily mean that it knows how to forward packets originating from PC1 back to the remote network of PC3
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.2 - Routing Table Principles

## Slide 25: IP Routing Table Routing Table Entries
In the figure, the numbers identify the following information:
Route source - This identifies how the route was learned.
Destination network (prefix and prefix length) - This identifies the address of the remote network.
Administrative distance - This identifies the trustworthiness of the route source. Lower values indicate preferred route source.
Metric - This identifies the value assigned to reach the remote network. Lower values indicate preferred routes.
Next-hop - This identifies the IP address of the next router to which the packet would be forwarded.
Route timestamp - This identifies how much time has passed since the route was learned.
Exit interface - This identifies the egress interface to use for outgoing packets to reach their final destination.
Note: The prefix length of the destination network specifies the minimum number of far-left bits that must match between the IP address of the packet and the destination network (prefix) for this route to be used.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.3 - Routing Table Entries

## Slide 26: IP Routing Table Directly Connected Networks
To learn about any remote networks, the router must have at least one active interface configured with an IP address and subnet mask (prefix length). This is known as a directly connected network or a directly connected route. Routers add a directly connected route to its routing table when an interface is configured with an IP address and is activated.
A directly connected network is denoted by a status code of C in the routing table. The route contains a network prefix and prefix length.
The routing table also contains a local route for each of its directly connected networks, indicated by the status code of L.
For IPv4 local routes the prefix length is /32 and for IPv6 local routes the prefix length is /128. This means the destination IP address of the packet must match all the bits in the local route for this route to be a match. The purpose of the local route is to efficiently determine when it receives a packet for the interface instead of a packet that needs to be forwarded.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.4 - Directly Connected Networks

## Slide 27: IP Routing Table Static Routes
After directly connected interfaces are configured and added to the routing table, static or dynamic routing can be implemented for accessing remote networks. Static routes are manually configured. They define an explicit path between two networking devices. They are not automatically updated and must be manually reconfigured if the network topology changes.
Static routing has three primary uses:
  It provides ease of routing table maintenance in smaller networks that are not expected to grow significantly.
  It uses a single default route to represent a path to any network that does not have a more specific match with another route in the routing table. Default routes are used to send traffic to any destination beyond the next upstream router.
  It routes to and from stub networks. A stub network is a network accessed by a single route, and the router has only one neighbor.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.5 - Static Routes

## Slide 28: IP Routing Table Static Routes in the IP Routing Table
The topology in the figure is simplified to show only one LAN attached to each router. The figure shows IPv4 and IPv6 static routes configured on R1 to reach the 10.0.4.0/24 and 2001:db8:acad:4::/64 networks on R2.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.6 - Static Routes in the IP Routing Table

## Slide 29: IP Routing Table Dynamic Routing Protocols
Dynamic routing protocols are used by routers to automatically share information about the reachability and status of remote networks. Dynamic routing protocols perform several activities, including network discovery and maintaining routing tables.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.7 - Dynamic Routing Protocols

## Slide 30: IP Routing Table Dynamic Routes in the Routing Table
OSPF is now being used in our sample topology to dynamically learn all the networks connected to R1 and R2. The routing table entries use the status code of O to indicate the route was learned by the OSPF routing protocol. Both entries also include the IP address of the next-hop router, via ip-address.
Note: IPv6 routing protocols use the link-local address of the next-hop router.
Note: OSPF routing configuration for IPv4 and IPv6 is beyond the scope of this course.
R1# show ip route
Codes: L - local, C - connected, S - static, R - RIP, M - mobile, B - BGP D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
(output omitted for brevity)
O 10.0.4.0/24 [110/50] via 10.0.3.2, 00:24:22, Serial0/1/1
O 10.0.5.0/24 [110/50] via 10.0.3.2, 00:24:15, Serial0/1/1
R1# show ipv6 route
IPv6 Routing Table - default - 10 entries
(Output omitted)
NDr - Redirect, RL - RPL, O - OSPF Intra, OI - OSPF Inter
O 2001:DB8:ACAD:4::/64 [110/50]
via FE80::2:C, Serial0/1/1
O 2001:DB8:ACAD:5::/64 [110/50]
via FE80::2:C, Serial0/1/1
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.8 - Dynamic Routes in the Routing Table

## Slide 31: IP Routing Table Default Route
The default route specifies a next-hop router to use when the routing table does not contain a specific route that matches the destination IP address. A default route can be either a static route or learned automatically from a dynamic routing protocol. A default route has an IPv4 route entry of 0.0.0.0/0 or an IPv6 route entry of ::/0. This means that zero or no bits need to match between the destination IP address and the default route.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.9 - Default Route

## Slide 32: IP Routing Table Structure of an IPv4 Routing Table
IPv4 was standardized using the now obsolete classful addressing architecture. The IPv4 routing table is organized using this same classful structure. Although the lookup process no longer uses classes, the structure of the IPv4 routing table still retains in this format.
An indented entry is known as a child route. A route entry is indented if it is the subnet of a classful address (class A, B or C network). Directly connected networks will always be indented (child routes) because the local address of the interface is always entered in the routing table as a /32. The child route will include the route source and all the forwarding information such as the next-hop address.
The classful network address of this subnet will be shown above the route entry, less indented, and without a source code. That route is known as a parent route.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.10 - Structure of an IPv4 Routing Table

## Slide 33: IP Routing Table Structure of an IPv4 Routing Table
An indented entry is known as a child route. A route entry is indented if it is the subnet of a classful address (class A, B or C network).
Directly connected networks will always be indented (child routes) because the local address of the interface is always entered in the routing table as a /32.
The child route will include the route source and all the forwarding information such as the next-hop address.
The classful network address of this subnet will be shown above the route entry, less indented, and without a source code. That route is known as a parent route.
Router# show ip route
(Output omitted)
192.168.1.0/24 is variably..
C 192.168.1.0/24 is direct..
L 192.168.1.1/32 is direct..
O 192.168.2.0/24 [110/65]..
O 192.168.3.0/24 [110/65]..
192.168.12.0/24 is variab..
C 192.168.12.0/30 is direct..
L 192.168.12.1/32 is direct..
192.168.13.0/24 is variably..
C 192.168.13.0/30 is direct..
L 192.168.13.1/32 is direct..
192.168.23.0/30 is subnette..
O 192.168.23.0/30 [110/128]..
Router#
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.10 - Structure of an IPv4 Routing Table

## Slide 34: IP Routing Table Structure of an IPv6 Routing Table
The concept of classful addressing was never part of IPv6, so the structure of an IPv6 routing table is very straight forward. Every IPv6 route entry is formatted and aligned the same way.
R1# show ipv6 route
(output omitted for brevity)
OE2 ::/0 [110/1], tag 2
via FE80::2:C, Serial0/0/1
C 2001:DB8:ACAD:1::/64 [0/0]
via GigabitEthernet0/0/0, directly connected
L 2001:DB8:ACAD:1::1/128 [0/0]
via GigabitEthernet0/0/0, receive
C 2001:DB8:ACAD:2::/64 [0/0]
via GigabitEthernet0/0/1, directly connected
L 2001:DB8:ACAD:2::1/128 [0/0]
via GigabitEthernet0/0/1, receive
C 2001:DB8:ACAD:3::/64 [0/0]
via Serial0/1/1, directly connected
L 2001:DB8:ACAD:3::1/128 [0/0]
via Serial0/1/1, receive
O 2001:DB8:ACAD:4::/64 [110/50]
via FE80::2:C, Serial0/1/1
O 2001:DB8:ACAD:5::/64 [110/50]
via FE80::2:C, Serial0/1/1
L FF00::/8 [0/0]
via Null0, receive
R1#
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.11 - Structure of an IPv6 Routing Table

## Slide 35: IP Routing Table Administrative Distance
A route entry for a specific network address (prefix and prefix length) can only appear once in the routing table. However, it is possible that the routing table learns about the same network address from more than one routing source. Except for very specific circumstances, only one dynamic routing protocol should be implemented on a router. Each routing protocol may decide on a different path to reach the destination based on the metric of that routing protocol.
This raises a few questions, such as the following:
  How does the router know which source to use?
  Which route should it install in the routing table?
Cisco IOS uses what is known as the administrative distance (AD) to determine the route to install into the IP routing table. The AD represents the "trustworthiness" of the route. The lower the AD, the more trustworthy the route source.
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.12 - Administrative Distance

## Slide 36: IP Routing Table Administrative Distance (Cont.)
The table lists various routing protocols and their associated ADs.
Route Source | Administrative Distance
Directly connected | 0
Static route | 1
EIGRP summary route | 5
External BGP | 20
Internal EIGRP | 90
OSPF | 110
IS-IS | 115
RIP | 120
External EIGRP | 170
Internal BGP | 200
Notes: 14 - Routing Concepts
14.4 - IP Routing Table
14.4.12 - Administrative Distance (Cont.)
14.4.13 - Check Your Understanding - IP Routing Table

## Slide 37: Static and Dynamic Routing
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing

## Slide 38: Static and Dynamic Routing Static or Dynamic?
Static and dynamic routing are not mutually exclusive. Rather, most networks use a combination of dynamic routing protocols and static routes.
Static routes are commonly used in the following scenarios:
  As a default route forwarding packets to a service provider
  For routes outside the routing domain and not learned by the dynamic routing protocol
  When the network administrator wants to explicitly define the path for a specific network
  For routing between stub networks
Static routes are useful for smaller networks with only one path to an outside network. They also provide security in a larger network for certain types of traffic, or links to other networks that need more control.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.1 - Static or Dynamic?

## Slide 39: Static and Dynamic Routing Static or Dynamic? (Cont.)
Dynamic routing protocols are implemented in any type of network consisting of more than just a few routers. Dynamic routing protocols are scalable and automatically determine better routes if there is a change in the topology.
Dynamic routing protocols are commonly used in the following scenarios:
  In networks consisting of more than just a few routers
  When a change in the network topology requires the network to automatically determine another path
  For scalability. As the network grows, the dynamic routing protocol automatically learns about any new networks.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.1 - Static or Dynamic? (Cont.)

## Slide 40: Static and Dynamic Routing Static or Dynamic? (Cont.)
The table shows a comparison of some the differences between dynamic and static routing.
Feature | Dynamic Routing | Static Routing
Configuration complexity | Independent of network size | Increases with network size
Topology changes | Automatically adapts to topology changes | Administrator intervention required
Scalability | Suitable for simple to complex network topologies | Suitable for simple topologies
Security | Security must be configured | Security is inherent
Resource Usage | Uses CPU, memory, and link bandwidth | No additional resources needed
Path Predictability | Route depends on topology and routing protocol used | Explicitly defined by the administrator
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.1 - Static or Dynamic? (Cont.)

## Slide 41: Static and Dynamic Routing Dynamic Routing Evolution
Dynamic routing protocols have been used in networks since the late 1980s. One of the first routing protocols was RIP. RIPv1 was released in 1988, but some of the basic algorithms within the protocol were used on the Advanced Research Projects Agency Network (ARPANET) as early as 1969. As networks evolved and became more complex, new routing protocols emerged.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.2 - Dynamic Routing Evolution

## Slide 42: Static and Dynamic Routing Dynamic Routing Evolution (Cont.)
The table classifies the current routing protocols. Interior Gateway Protocols (IGPs) are routing protocols used to exchange routing information within a routing domain administered by a single organization.
There is only one EGP and it is BGP. BGP is used to exchange routing information between different organizations, known as autonomous systems (AS). BGP is used by ISPs to route packets over the internet. Distance vector, link-state, and path vector routing protocols refer to the type of routing algorithm used to determine best path.
 | Interior Gateway Protocols |  |  |  | Exterior Gateway Protocols
 | Distance Vector |  | Link-State |  | Path Vector
IPv4 | RIPv2 | EIGRP | OSPFv2 | IS-IS | BGP-4
IPv6 | RIPng | EIGRP for IPv6 | OSPFv3 | IS-IS for IPv6 | BGP-MP
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.2 - Dynamic Routing Evolution (Cont.)

## Slide 43: Static and Dynamic Routing Dynamic Routing Protocol Concepts
A routing protocol is a set of processes, algorithms, and messages that are used to exchange routing information and populate the routing table with the choice of best paths. The purpose of dynamic routing protocols includes the following:
  Discovery of remote networks
  Maintaining up-to-date routing information
  Choosing the best path to destination networks
  Ability to find a new best path if the current path is no longer available
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.3 - Dynamic Routing Protocol Concepts

## Slide 44: Static and Dynamic Routing Dynamic Routing Protocol Concepts (Cont.)
The main components of dynamic routing protocols include the following:
  Data structures - Routing protocols typically use tables or databases for their operations. This information is kept in RAM.
  Routing protocol messages - Routing protocols use various types of messages to discover neighboring routers, exchange routing information, and other tasks to learn and maintain accurate information about the network.
  Algorithm - An algorithm is a finite list of steps used to accomplish a task. Routing protocols use algorithms for facilitating routing information and for the best path determination.
Routing protocols determine the best path, or route, to each network. That route is then offered to the routing table. The route will be installed in the routing table if there is not another routing source with a lower AD.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.3 - Dynamic Routing Protocol Concepts (Cont.)

## Slide 45: Static and Dynamic Routing Best Path
The best path is selected by a routing protocol based on the value or metric it uses to determine the distance to reach a network. A metric is the quantitative value used to measure the distance to a given network. The best path to a network is the path with the lowest metric.
Dynamic routing protocols typically use their own rules and metrics to build and update routing tables. The following table lists common dynamic protocols and their metrics.
Routing Protocol | Metric
Routing Information Protocol (RIP) | The metric is “hop count”. Each router along a path adds a hop to the hop count. A maximum of 15 hops allowed.
Open Shortest Path First (OSPF) | The metric is “cost” which is the based on the cumulative bandwidth from source to destination. Faster links are assigned lower costs compared to slower (higher cost) links.
Enhanced Interior Gateway Routing Protocol (EIGRP) | It calculates a metric based on the slowest bandwidth and delay values. It could also include load and reliability into the metric calculation.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.4 - Best Path

## Slide 46: Static and Dynamic Routing Load Balancing
When a router has two or more paths to a destination with equal cost metrics, then the router forwards the packets using both paths equally. This is called equal cost load balancing.
The routing table contains the single destination network, but has multiple exit interfaces, one for each equal cost path. The router forwards packets using the multiple exit interfaces listed in the routing table.
If configured correctly, load balancing can increase the effectiveness and performance of the network.
Equal cost load balancing is implemented automatically by dynamic routing protocols. It is enabled with static routes when there are multiple static routes to the same destination network using different next-hop routers.
Note: Only EIGRP supports unequal cost load balancing.
Notes: 14 - Routing Concepts
14.5 - Static and Dynamic Routing
14.5.5 - Load Balancing
14.5.6 - Check Your Understanding - Dynamic and Static Routing

## Slide 47: Module Practice and Quiz
Notes: 14 - Routing Concepts
14.6 - Module Practice and Quiz

## Slide 48: Quick Review Question
Refer to Quiz - Chapter 14 in Cisco Networking Academy platform
In this Packet Tracer, you will complete the following:
  Configure Static and Dynamic Routing Protocols

## Slide 49
Routers learn about remote networks in two ways: static routes and with dynamic routing protocols.
After a router determines the correct path, it can forward the packet on a directly connected network, it can forward the packet to a next-hop router, or it can drop the packet.
Routers support three packet forwarding mechanisms: process switching, fast switching, and CEF.
There are several configuration and verification commands for routers, including show ip route, show ip interface, show ip interface brief and show running-config.
Routing table entries include the route source, destination network, AD, metric, next-hop, route timestamp, and exit interface.
Static routes are manually configured and define an explicit path between two networking devices.
Summary of Main Teaching Points

## Slide 50
Dynamic routing protocols can discover a network, maintain routing tables, select a best path, and automatically discover a new best path if the topology changes.
The default route specifies a next-hop router to use when the routing table does not contain a specific route that matches the destination IP address. A default route can be either a static route or learned automatically from a dynamic routing protocol.
Dynamic routing protocol are commonly used in networks consisting of more than just a few routers, when a change in the network topology requires the network to automatically determine another path, and for scalability. As the network grows, the dynamic routing protocol automatically learns about any new networks.
Current routing protocols include IGPs and EGPs. IGPs exchange routing information within a routing domain administered by a single organization. The only EGP is BGP. BGP exchanges routing information between different organizations.BGP is used by ISPs to route packets over the internet.
Summary of Main Teaching Points

## Slide 51: Question and Answer Session
Q & A

## Slide 52: What we will cover next
DHCPV4