## Slide 1: System and Network Administration
Network Essentials

## Slide 2: Configuring for Network Services
Networks are made of
Hosts that act as clients and servers
  Servers share resources with AUTHORISED Clients
Media and Equipment that interconnect hosts
Protocols that govern connections
Users
Networks allow cooperation
Cooperation leads to communities of users

## Slide 3: Network Components
Component | Description
Device | Any piece of hardware such as a computer, server, printer, or smartphone.
Media | Connects devices to the network and carries data between devices.
Network adapter | Hardware that translates data between the network and a device.
Operating system | Software that controls network traffic and access to network resources.
Protocol | Software that controls network communications using a set of rules.

## Slide 5: ISO OSI Reference Model
Each layer represents a higher level of abstraction in the process of data communications
Complexities of low level transmission of signals representing the data are hidden from users at the application level (top layer)
Understanding the abstract architecture is key to understanding the concrete network
The ISO Seven “layer” OSI Model is a Conceptual model that describes many types of network.
The Internet is a fairly unsophisticated example.

## Slide 6: OSI Model: Information Flow
Provides network services to user applications
Coding and conversion to ensure both ends use a common data format
Establish, maintain, & terminate the “conversation” between endpoint processes
Process ID, Error detection, Flow control
Network Addressing & Routing
Interface Address, Error detection, Flow control
Voltage levels, Maximum transmission distances, Physical connectors
6. Presentation
7. Application
1. Physical
2. Data-Link
3. Network
4. Transport
5. Session
6. Presentation
7. Application
1. Physical
2. Data-Link
3. Network
4. Transport
5. Session
“Please Do Not Throw Snow Peas Away”

## Slide 7: OSI
6. Presentation
7. Application
1. Physical
2. Data-Link
3. Network
4. Transport
5. Session
TCP/IP
Understanding the abstract architecture is key to understanding the concrete network
For this class the concrete network is TCP/IP over Ethernet
5. Application
3. Internet
4. Transport
2. Network
Access
1. Physical
Secure Sockets Layer (SSL)
TCP: Handshake, Port, Sequence
IP: Source & Destination Address, Subnets, Routing
Link Layer Control (LLC)
Ethernet: CSMA/CD - Broadcast
Media Access Control (MAC) Address

## Slide 8: 7 Layers to 5
Presentation Layer
The Presentation Layer is for providing a standard way of encoding data, including encryption and character encoding (unicode).
MIME (Multipurpose Internet Mail Extensions) is a Presentation Layer protocol that defines the formatting of e-mail messages
Presentation Layer functions are most commonly implemented as part of the Application Layer.
Session Layer
The session layer creates and terminates unique connections.
TCP implements some session layer functionality (since it maintains connection states using sequence number).
Session layer services are most commonly implemented as part of the Application layer. For example, HTTP is is a "stateless" protocol and a web application uses PHP or .NET for “session cookies”.

## Slide 10: Packets and Encapsulation
Packets: Header and payload
  Header tells where the packet came from and where it’s going
  Payload is the data
  TCP layer it’s called a segment
  IP layer it’s called a packet
  Link layer it’s called a frame
Cultural
Sensitivity

## Slide 11: Encapsulation
A packet is a structured message.
The control information of a given protocol must be treated strictly as data by the next "lower" protocol.
As a packet moves down the protocol stack, it gets bigger as information relevant to the layer is added to the beginning and the end.
Any given layer is allowed to work only with the data relevant to that layer, and nobody else's.
As a packet moves up the stack it gets smaller, as the information from the current level is removed.

## Slide 12
Ethernet, IP, and TCP
TCP Segment
Header
Data
IP Datagram Header
Complete TCP Segment
Treated as Data
Frame Header
CRC
Complete IP Datagram
Treated as Data
Remember, this is really just a stream of bits
0011110101010101110000101010101010001010110101001001010100101110010100

## Slide 13
Preamble (64 bits)
Destination Address (48 bits)
Source Address (48 bits)
Packet type (16 bits)
Data (368-12,000 bits)
CRC (32 bits)
Ethernet Frame Format
Key Fields
Preamble: Alternating 1's and 0's to help receiving nodes synchronise
Address: Unique identifier assigned by the hardware manufacturer (MAC Address)
Packet Type: identifies this as an Ethernet frame (allows mutiple protocols and versions)
CRC: Error detection (Cyclic Redundancy Check)
Remember, this is really just a stream of bits
0011110101010101110000101010101010001010110101001001010100101110010100

## Slide 14
Datagram Format Each row represents 4 octets (32 bits)
Version - Length - QOS - Total Length
Unique ID - Flags - Fragment Offset
Time to Live - Protocol - Checksum
Source IP Address
Destination IP Address
Options - Padding
Data (up to 4416 bits)
Key Fields
IP is version 4 or 6
QOS requests priority
Second Row controls Fragmentation (e.g., "2 of 4")
Gateways decrement TTL and discard the datagram if zero
Protocol is analogous to Ethernet Type, Header Checksum to CRC
Options are included for network testing (not required)
Remember, this is really just a stream of bits
0011110101010101110000101010101010001010110101001001010100101110010100

## Slide 15
TCP Segment Format Each row represents 4 octets (32 bits)
Acknowledgement Number
Options - Padding
Source Port - Destination Port
Sequence Number
Offset - Code - Window
Checksum - Urgent
Data (up to 4224 bits)
Key Fields
Port number specifies service
Sequence is position in sender's byte stream
Acknowledgement of position in sender's byte stream
Some segments carry only ACK, others carry data, and others a request to establish or close a connection (Code)
Window and Options negotiate maximum segment size
Remember, this is really just a stream of bits
0011110101010101110000101010101010001010110101001001010100101110010100

## Slide 16
TCP Segment
Header
Data
IP Datagram Header
Complete TCP Segment
Treated as Data
Frame Header
CRC
Complete IP Datagram
Treated as Data
Data Link Layer: stream of bits
0011110101010101110000101010101010001010110101001001010100101110010100
Am I a Router? Yes: Pass the whole packet to all interfaces No: ~
Is this an ethernet frame? Yes: Pass it up No: discard it
Is this my MAC address? Yes: Pass up the DATA part No: discard it
Is there a service on this port? Yes: Pass up the DATA part No: discard it
Is this my IP address? Yes: Pass up the DATA part No: discard it
Ethernet, IP, and TCP

## Slide 19
HTTP | Identical Message (end-to-end) |  |  |  | HTTP
TCP | Identical Segments (end-to-end) |  |  |  | TCP
IP | Identical Datagram | Intermediate Router (Layer 3) or Switch (Layer 2) |  | Identical Datagram | IP
Ethernet | Proper Frame |  |  | Proper Frame | Ethernet
Network Interface | Wiring | Network Interface | Network Interface | Wiring | Network Interface
  Switching is the process of taking an incoming frame from one interface and delivering it out through another interface.
  At Layer 2 frames are switched based on MAC address
  At Layer 3 packets are switched based on IP address
Host A
Host B
Beyond a broadcast domain, communication is typically through a network of intermediate switching nodes.

## Slide 20: TinyNet in practice

## Slide 21: Virtual Networking
VirtualBox provides Layer 2 (Network Access) interconnection
A hub broadcasts every message to every interface
We can watch this with a packet sniffer when we put the interface into promiscuous mode
TinyNet
Layer 2

## Slide 22: Virtual Networking
Layer 3 (Internet) interconnection is more useful
Assign an IP address to each interface
Configure a default or static route to the gateway
Gateway interconnects subnets
TinyNet
Layer 3

## Slide 23: IP Addressing & Subnet Masks
Subnet Mask is like an IPv4 Address: 32 bits long
Specifies which part of an IP address is the network/subnet field and which part is the host field
The prefix portion of the mask is all 1s in binary.
The host portion of the mask is all 0s in binary.

## Slide 24: Classless Addressing (VLSM)
Extend the network prefix by borrowing bits from host address range
  a Variable Length Subnet Mask (VLSM)
An IP address is accompanied by an indication of the prefix length
  192.168.11.0 255.255.255.0
    Convert the binary expression to dotted-decimal notation
  192.168.11.0/24
    / specifies the number of ones “up front”
Contiguous subnet mask: no 1 bit appears to the right of any 0 bit

## Slide 25
Network | Netmask
172.16.20.0 | 255.255.255.0
172.16.30.0 | 255.255.255.0
172.16.40.0 | 255.255.255.0
Delta
172.16.40.0
172.16.20.0
172.16.30.0
Beta
Alpha
Iota
172.16.20.2
172.16.40.1
172.16.20.1
172.16.40.2
172.16.30.1
172.16.30.2
This network has 3 subnets
The routing table actually has both the IP address and the netmask
You cannot tell what subnet an address belongs to without knowing the netmask!

## Slide 26: Addresses
Layer 2 addresses are put into the interface ROM by the hardware manufacturer
Layer 3 addresses are assigned by the network administrator
  If users move to another building (or WAP), their device may get a new Layer 3 address, but the Layer 2 address remains the same.
The broadcast domain is everyone who can hear a broadcast.
It is important to limit the size of the broadcast domain because too many broadcast frames can overwhelm endpoints, switches and routers
At layer 3 the broadcast domain is defined by the subnet mask.
At layer 2 a hub is a single broadcast domain, or switch ports are configured to define the broadcast domain (vlan tagging).

## Slide 27: Virtual Local Area Networks (VLANs)
Similar to subnets.
  However, subnets are network layer (layer 3).
VLANs enable grouping of network hosts not on the same physical switch or multiple VLANs on the same physical switch.
If network configuration changes, the physical cabling and devices don't need to.
VLANs can be configured with one or more subnets.
A logical method of segmenting a network at the data link layer (layer 2) – Also called VLAN Tagging.

## Slide 29: Internet Protocols and Standards
Ethernet
Application
Transport
Internet
Network
Access
ICMP
TCP
UDP
IP
/etc/services
ARP
IETF: Internet Engineering Task Force
IEEE: Institute of Electrical and Electronic Engineers
IANA: Internet Assigned Numbers Authority
And Others
RFC: Request For Comments
ITU: International Telecommunications Union

## Slide 30: ARP - Address Resolution Protocol
Concerned with mapping layer 2 to layer 3 addresss, e.g., MAC address to IP address.
The source host sends an ARP request by broadcast, asking “who has IP address A.B.C.D?”
If the destination host (which owns A.B.C.D) sees the ARP query, it responds and sends its MAC address.
If the destination host is not on the same local network, the router/gateway will respond and send its own MAC address.
The source host registers the MAC address obtained and a data-link (layer 2) connection is established between the two hosts.
Notes: Network Admin - Internet Services
3/22/2022
30

## Slide 31
Source IP: 192.168.6.101
Source MAC: 1a:2b:3c:4d:5e:6f
Target IP: 192.168.6.1
Target MAC: a1:b2:c3:d4:e5:f6
arp Reply
Source IP: 192.168.6.1
Source MAC: a1:b2:c3:d4:e5:f6
Target IP: 192.168.6.101
Target MAC: 00:00:00:00:00:00
arp Request
ARP - Address Resolution Protocol
Any reply is cached, even if no request was sent. Attackers can easily substitute their MAC and divert traffic.
ARP Spoofing relies on the decentralized, unauthenticated, and completely trusting nature of ARP

## Slide 32
Used for gateway management:
congestion control (source quench)
route-change notification (redirect)
subnet addressing (address mask request/reply)
Also for general network management:
reachability testing (echo request/reply)
performance measuring (timestamp)
ICMP - Internet Control Message Protocol
Notes: Network Admin - Internet Services
3/22/2022
32

## Slide 33: ping
Used to check a target host for a response.
Many systems block ICMP to prevent attacks:
  Flood system in a Smurf attack.
  Reconfigure routing tables with forged packets.
Uses ICMP “echo request” and “echo reply” to check network connectivity.
Echo request
1
2
Echo reply
192.168.0.154
Is 192.168.0.154 reachable?

## Slide 34: UDP - User Datagram Protocol
Connectionless service for application level procedures
  Unreliable: delivery not guaranteed & no duplication control
Reduced overhead, least common denominator service
Used when one IP packet is sufficient for the whole message
  DNS tries to use UDP first, fallback to TCP
Notes: 34
In addition to TCP, there is one other transport-level protocol that is in common use as part of the TCP/IP protocol suite: the user datagram protocol (UDP), specified in RFC 768. UDP provides a connectionless service for application-level procedures. UDP is basically an unreliable service; delivery and duplicate protection are not guaranteed. However, this does reduce the overhead of the protocol and may be adequate in many cases. A connectionless service is more appropriate in some contexts. It represents a "least common denominator" of service to be expected at higher layers. Some examples:
• Inward data collection: the periodic active or passive sampling of data sources, such as sensors, and automatic self-test reports from security equipment or network components.
• Outward data dissemination: Includes broadcast messages to network users, the announcement of a new node or the change of address of a service, and the distribution of real-time clock values.
• Request-response: in which a transaction service is provided by a common server to a number of distributed TS users, and for which a single request-response sequence is typical. Use of the service is regulated at the application level, and lower-level connections are often unnecessary and cumbersome.
• Real-time applications: Such as voice and telemetry, involving a degree of redundancy and/or a real-time transmission requirement. These must not have connection-oriented functions such as retransmission.
Network Admin - Internet Services

## Slide 35: TCP: Transmission Control Protocol
TCP connections provide reliable delivery for messages that are too big for a single packet
The message is broken into a number of packets before it is sent
Packets can arrive in any order, missing packets are re-sent
Packet sequence numbers are established during the initial connection using a “3-Way Handshake”.
Other initial connection setup messages establish parameters of channel e.g., buffer sizes, error detection & recovery procedures.
Notes: FIT2018 Network Admin: Principles of Security
22/03/2022
FIT2018 (c) Monash University
35

## Slide 37: Ports and Port Ranges
Client computers connect to server programs through a designated port.
Port is a “Layer 4” concept – TCP header
All ports assigned are between the numbers 0 and 65535.
Port: The endpoint of a logical network connection.
Port | Service
53 | DNS
67 | DHCP (server)
68 | DHCP (client)
587 | Submission
Port | Service | Secure | Port
20 | Telnet | SSH | 22
25 | SMTP | SMTPS | 465
80 | HTTP | HTTPS | 443
143 | IMAP | IMAPS | 993
389 | LDAP | LDAPS | 636

## Slide 38: Service names and port numbers
Service names and port numbers are used to distinguish between different services that run over TCP and UDP (transport layer)
A port is actually just a 16 bit number used as an identifier
The registration procedures for service names and port numbers are described in [RFC6335].
Service names are assigned by IANA with a first-come, first-served process.

## Slide 39: Transport Protocol Addresses: TCP & UDP Port Numbers
# This file contains port numbers for well-known services defined by IANA
# Format:
# <service name> <port number>/<protocol> [aliases...] [#<comment>]
discard 9/tcp sink null
discard 9/udp sink null
qotd 17/tcp quote #Quote of the day
qotd 17/udp quote #Quote of the day
ftp-data 20/tcp #FTP, data
ftp 21/tcp #FTP. control
telnet 23/tcp
smtp 25/tcp mail #Simple Mail Transfer Protocol
time 37/tcp timserver
time 37/udp timserver
domain 53/tcp #Domain Name Server
domain 53/udp #Domain Name Server
bootps 67/udp dhcps #Bootstrap Protocol Server
bootpc 68/udp dhcpc #Bootstrap Protocol Client
tftp 69/udp #Trivial File Transfer
finger 79/tcp
http 80/tcp www www-http #World Wide Web
/etc/services
Notes: Look for /etc/services on Unix systems and C:\windows\system32\drivers\etc\services on Windows.
Network Admin - Internet Services
3/22/2022
39

## Slide 40
Port numbers are assigned based on three ranges:
The Well Known or System Ports (0-1023)
  Ports under 1024 restricted to root
The Registered or User Ports (1024-49151),
The Dynamic and/or Private Ports (49152-65535);
System Ports are assigned by IETF for standards-track protocols, User Ports are assigned by IANA, and dynamic ports are not assigned.